## Slide 1
Network-on-Chip
(1/2)
Ben Abdallah Abderazek
The University of Aizu
E-mail: benab@u-aizu.ac.jp
Hong Kong University of Science and Technology, March 2013

## Slide 2: Part 1 Application requirements NoC: A paradigm shift in VLSI Design Critical problems addressed by NoC Traffic abstractions Data abstraction Network delay modeling

## Slide 3: Application Requirements
Signal processing
Hard real time
Very regular load
High quality
Typically on DSPs
Media processing
Hard real time
Irregular load
High quality
SoC/media processors
Multimedia
Soft real time
Irregular load
Limited quality
PC/desktop
Very challenging.

## Slide 4: Packet Processing in Future Internet
Multicore System-on-Chip (MCSoC):
  High processing power
  Support wire speed
  Programmable
  Scalable
  Wide applications in networking areas
More packets
&
Complex packet
processing
General Purpose
Processors
ASIC
(large, expensive to
develop,
not flexible)
Future Internet
MCSoC

## Slide 5: Telecommunication Systems & NoC
The trend nowadays is to integrate telecommunication system on complex MCSoC:
  Network processors,
  Multimedia hubs, and
  base-band telecom circuits
These applications have tight time-to-market and performance constraints

## Slide 6: Typical NP (Network Processor)

## Slide 7: Examples of NP Applications

## Slide 8: Telecommunication System Requirements
A typical telecommunication system is composed of 4 type of components:
  Software tasks
  Processors executing software
  Specific hardware cores, and
  Global on-chip communication network

## Slide 9: Telecommunication System Requirements
A typical telecommunication system is composed of 4 types of components:
  Software tasks
  Processors executing software
  Specific hardware cores, and
  Global on-chip communication network
This is on of the most challenging issue.

## Slide 10: Technology & Architecture Trends
Technology trends
  Vast transistor budgets
  Relatively poor interconnect scaling
  Need to manage complexity and power
  Build flexible designs (multi-/general-purpose)
Architectural trends
  Go parallel!

## Slide 11
Information transfer is inherently unreliable at the electrical level, due to:
  Timing errors
  Cross-talk
  Electro-magnetic interference (EMI)
  Soft errors
The problem will get increasingly worse as technology scales down
Communication Reliability

## Slide 12
Operation | Delay (.13mico) | Delay (.05micro)
32-bit ALU Operation | 650ps | 250ps
32-bit Register read | 325ps | 125ps
Read 32-bit from 8KB RAM | 780ps | 300ps
Transfer 32-bit across chip (10mm) | 1400ps | 2300ps
Transfer 32-bit across chip (200mm) | 2800ps | 4600ps
2:1 global on-chip communication to operation delay 9:1 in 2010
Ref: W.J. Dally HPCA Panel presentation 2002
Wire Delay vs. Logic Delay

## Slide 13: On-chip Interconnection Types
Point-to-Point
Many
Modules
M1
I/O2
P1
P1
P3
I/O1
P2
P5
M3
M2
I/O
P1
P2
M1
P3
-Leakage Power
-Thermal Power
-Noise

## Slide 14: On-chip Interconnection Types
Shared bus
P1
I/O
2
P2
P3
M1
P4
M2
I/O
1
P5
P6
M3
I/O
3
P7
M4
Wait
Wait
Wait
Wait
Wait
Wait

## Slide 15: On-chip Interconnection Types
Hierarchical bus
P3
M1
P4
M2
M3
I/O
3
P7
M4
P1
I/O
2
P2
I/O
1
P5
P6
Wait
Wait
Wait
Wait
Wait
Bridge

## Slide 16: On-chip Interconnection Types
Bus matrix
P2
M1
P1
M2
P3
M3
I/O
1
P6
P5
P4
Wait
Wait

## Slide 17: On-chip Interconnection Types
Network-on-Chip -> our main topic in this lecture.
Processing
element
Network
Interface
Router
Input
buffers
Unidirectional
links

## Slide 18: On-chip Interconnection Types
Network-on-Chip -> our main topic in this lecture

## Slide 19
Let us Summarize all On-chip Interconnection Types
Ref.: Abderazek Ben Abdallah, Multicore Systems-on-Chip: Practical Hardware/Software Design, 2nd Edition, Publisher: Springer, (2013) , ISBN-13: 978-9491216916

## Slide 20: Traditional SoC Nightmare
Variety of dedicated interfaces
Design and verification complexity
Unpredictable performance
Many underutilized wires
DMA
CPU
DSP
Bridge
IO
IO
IO
C
A
B
Peripheral Bus
CPU Bus
Control
signals

## Slide 21: NoC: A paradigm Shift in VLSI
s
s
s
s
s
s
s
s
Module
Module
s
Module
From: Dedicated signal wires
To: Shared network
Point-
To-point
Link
Network
switch
Computing
Module

## Slide 22: NoC: A paradigm Shift in VLSI
NI
DRAM
switch
NI
CPU
Accel
NI
switch
switch
switch
NoC
switch
switch
NI
DRAM
Coproc
I/O
NI
NI
NI
NI
NI
NI
NI
NI
DSP
DMA
MPEG
DMA
Ethnt
Ethnt

## Slide 23: NoC Essential
Communication by packets of bits
Routing of packets through several hops via switches
Efficient sharing of wires
Parallelism
s
s
s
s
s
s
s
s
Module
Module
s
Module

## Slide 24: NoC Operation Example
CPU request
Packetization and trans.
Routing
Receipt and unpacketization (AHB, OCP, ... pinout)
Device response
Packetization and transmission
Routing
Receipt and unpacketization
CPU
I/O
Network Interface
switch
Network Interface
switch
switch

## Slide 25: Characteristics of a Paradigm Shift
Solves a critical problem
Step-up in abstraction
Design is affected:
  Design becomes more restricted
  New tools
  The changes enable higher complexity and capacity
  Jump in design productivity

## Slide 26: Characteristics of a Paradigm shift
Solves a critical problem
Step-up in abstraction
Design is affected:
  Design becomes more restricted
  New tools
  The changes enable higher complexity and capacity
  Jump in design productivity
We will look at the problem addressed by NoC.

## Slide 27: Don't we already know how to design interconnection networks?
Many existing network topologies, router designs and theory has already been developed for high end supercomputers and telecom switches
Yes, and we'll cover some of this material, but the trade-offs on-chip lead to very different designs!!
27

## Slide 28: Critical problems addressed by NoC
1) Global interconnect design problem:
delay, power, noise, scalability, reliability
2) System integration
productivity problem
3) Multicore Processors
key to power-efficient computing

## Slide 29: 1(a): NoC and Global wire delay
Long wire delay is dominated by Resistance
Add repeaters
Repeaters become latches (with clock frequency scaling)
Latches evolve to NoC routers
NoC Router
NoC Router
NoC Router

## Slide 30: 1(b): Wire design for NoC
NoC links:
  Regular
  Point-to-point (no fanout tree)
  Can use transmission-line layout
  Well-defined current return path
Can be optimized for noise /speed/power ?
  Low swing,
  current mode,
  ….

## Slide 31: 1(c): NoC Scalability
NoC:
O(n)
O(n)
Point –to-Point
O(n^2 √n)
O(n √n)
Simple Bus
O(n^3 √n)
O(n√n)
Segmented Bus:
O(n^2 √n)
O(n√n)
For Same Performance, compare the wire area and power

## Slide 32: 1(d): NoC and Communication Reliability
Router
UMODEM
U
MO
D
E
M
UMODEM
U
MO
D
E
M
Router
UMODEM
U
MO
D
E
M
UMODEM
U
MO
D
E
M
Router
 | … |  | 
Error correction
Synchronization
ISI reduction
Parallel to Serial Convertor
Modulation
Link Interface
Interconnect
Input buffer
m
n
Fault tolerance & error correction
A. Morgenshtein, E. Bolotin, I. Cidon, A. Kolodny, R. Ginosar, “Micro-modem – reliability solution for NOC communications”, ICECS 2004

## Slide 33: 1(e): NoC and GALS
Modules in NoC use different clocks
  May use different supply voltages
NoC can handle synchronization
NoC design may be asynchronous
  No waste of power when the links and routers are idle

## Slide 34: 2: NoC and Engineering Productivity
NoC eliminates ad-hoc global wire engineering
NoC separates computation from communication
NoC is a complete platform for system integration, debugging and testing

## Slide 35: 3: NoC and Multicore
Uniprocessors cannot provide Power-efficient performance growth
  Interconnect dominates dynamic power
  Global wire delay doesn’t scale
  ILP is limited
Gate
Interconnect
Diff.

## Slide 36: 3: NoC and Multicore
Power-efficiency requires many parallel local computations
  Multicore chip
  Thread-Level Parallelism (TLP)
Uniprocessor Performance
Die Area (or Power)

## Slide 37: 3: NoC and Multicore
Uniprocessors cannot provide Power-efficient performance growth
  Interconnect dominates dynamic power
  Global wire delay doesn’t scale
  Instruction-level parallelism is limited
Power-efficiency requires many parallel local computations
  Chip Multi Processors (CMP)
  Thread-Level Parallelism (TLP)
Network is a natural choice for CMP!

## Slide 38: 3: NoC and Multicore
Uniprocessors cannot provide Power-efficient performance growth
  Interconnect dominates dynamic power
  Global wire delay doesn’t scale
  Instruction-level parallelism is limited
Power-efficiency requires many parallel local computations
  Chip Multi Processors (CMP)
  Thread-Level Parallelism (TLP)
Network is a natural choice for CMP!
Network is a natural choice for Multicore

## Slide 39: Why now is the time for NoC ?
Difficulty of DSM wire design
Productivity pressure
Multicore

## Slide 40: Layers of Abstraction in Network Modeling
Software layers
  Application, OS
Network & transport layers
  Network topology e.g. crossbar, ring, mesh, torus, fat tree,…
  Switching Circuit / packet switching(SAF, VCT), wormhole
  Addressing Logical/physical, source/destination, flow, transaction
  Routing Static/dynamic, distributed/source, deadlock avoidance
  Quality of Service e.g. guaranteed-throughput, best-effort
  Congestion control, end-to-end flow control

## Slide 41: Layers of Abstraction in Network Modeling
Data link layer
  Flow control
  Handling of contention
  Correction of transmission errors
Physical layer
  Wires, drivers, receivers, repeaters, signaling, circuits,..

## Slide 42: How to Select Architecture ?
ASIC
FPGA
ASSP
CMP/
Multicore
Reconfiguration
Rate
During run time
At boot time
At design time
Single application General purpose or Embedded systems
Flexibility
Architecture choices depends on system needs

## Slide 43: How to Select Architecture ?
ASIC
FPGA
ASSP
CMP/
Multicore
Reconfiguration
Rate
During run time
At boot time
At design time
Single application General purpose or Embedded systems
Flexibility
A large range of solutions!
Architecture choices depends on system needs

## Slide 44: Perspective 1: NoC vs. Bus
Aggregate bandwidth grows
Link speed unaffected by N
Concurrent spatial reuse
Pipelining is built-in
Distributed arbitration
Separate abstraction layers
However:
No performance guarantee
Extra delay in routers
Area and power overhead?
Modules need NI
Unfamiliar methodology
Bandwidth is shared
Speed goes down as N grows
No concurrency
Pipelining is tough
Central arbitration
No layers of abstraction
(communication and computation are coupled)
However:
Fairly simple and familiar
NoC
Bus

## Slide 45: Perspective 2: NoC vs. Off-chip Networks
Cost is in the links
Latency is tolerable
Traffic/applications unknown
Changes at runtime
Adherence to networking standards
Sensitive to cost:
  area
  power
Wires are relatively cheap
Latency is critical
Traffic may be known a-priori
Design time specialization
Custom NoCs are possible
Off-Chip Networks
NoC

## Slide 46: VLSI CAD Problems
Application mapping
Floorplanning (placement)
Routing
Buffer sizing
Timing closure
Simulation
Testing

## Slide 47: VLSI CAD Problems in NoC
Application mapping (map tasks to cores)
Floorplanning (within the network)
Routing (of messages)
Buffer sizing (size of FIFO queues in the routers)
Simulation (Network simulation, traffic/delay/power modeling)
Other NoC design problems (topology synthesis, switching, virtual channels, arbitration, flow control,……)

## Slide 48: Traffic Abstractions
Traffic model are generally captured from actual traces of functional simulation
A statically distribution is often assumed for message
PE1
PE2
PE3
PE4
PE12
PE11
PE5
PE9
PE7
PE8
PE6
PE10

## Slide 49: Data Abstractions
Packet | Packet | Packet | Packet
Message
Head Flit | Body Flit | Body Flit | Tail Flit
Packet
Type | Sequence # | VC | data
Flit
Phit

## Slide 50: Typical NoC Design Flow
Determine routing and adjust link capacities

## Slide 51: Timing Closure in NoC
Define inter-module traffic
Place modules
Increase link capacities
QoS satisfied ?
No
Yes
Finish
Too long capacity results in poor QoS
Too high capacity wastes area
Uniform link capacities are a waste in ASIP system

## Slide 52: NoC Design Requirements
High-performance interconnect
  High-throughput, latency, power, area
Complex functionality
  Support for virtual-channels
  QoS
Synchronization
  Reliability, high-throughput, low-latency

## Slide 53: Break + Questions

## Slide 54
Part II: NoC Building Blocks
Topology
Routing
Control Flow
Network Interface
Router Architecture

## Slide 55
Part II: NoC Building Blocks
Topology
Routing Algorithms
Routing Mechanisms
Control Flow
Network Interface
Router Architecture

## Slide 56: NoC Topology
Mainly adopted from large-scale networks and parallel computing
A good topology allows to fulfill the requirements of the traffic at reasonable costs
Topology classifications:
  Direct topologies
  Indirect topologies
NoC topology is the connection map
between PEs.
Notes: The ring is the least complex topology where router nodes are connected in a circular fashion, but scalability is poor due to limited connectivity.
Mesh: Meshes have a relatively large average network distance, which can increase power consumption. Moreover, concentrated areas of high traffic within the grid, called hotspots, may occur
The 2-D Torus is similar to a mesh, but extended with wrap-around links to reduce average network distance. A two-dimensional torus has a similar area footprint
as the mesh, with the overhead in added links.
An irregular topology can be derived by altering the connectivity of a regular topology
(i.e., one of the topologies described thus far), to form hybrid, cluster-based, or
asymmetric topologies

## Slide 57: Direct Topology: Mesh
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
R
R
R
R
R
R
R
R
PE
PE
PE
PE
R
R
R
R
R
R
R
R
Notes: The main problem with the mesh topology is its long diameter that has negative effect on communication latency.
Torus topology was proposed to reduce the latency of mesh and keep its simplicity.
The only difference between torus and mesh topologies is that the switches on the edges are connected to the switches on the opposite edges through wrap-around channels.

## Slide 58: Direct Topology: Torus
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
R
R
R
R
R
R
R
R
PE
PE
PE
PE
R
R
R
R
R
R
R
R
Notes: The main problem with the mesh topology is its long diameter that has negative effect on communication latency.
Torus topology was proposed to reduce the latency of mesh and keep its simplicity.
The only difference between torus and mesh topologies is that the switches on the edges are connected to the switches on the opposite edges through wrap-around channels.

## Slide 59: Direct Topology: Folded Torus
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
R
R
R
R
R
R
R
R
PE
PE
PE
PE
R
R
R
R
R
R
R
R
Fold
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
R
PE
R
PE
R
PE
R
PE
Notes: The main problem with the mesh topology is its long diameter that has negative effect on communication latency.
Torus topology was proposed to reduce the latency of mesh and keep its simplicity.
The only difference between torus and mesh topologies is that the switches on the edges are connected to the switches on the opposite edges through wrap-around channels.

## Slide 60: Direct Topology: Folded Torus
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
R
R
R
R
R
R
R
R
PE
PE
PE
PE
R
R
R
R
R
R
R
R
Fold
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
R
PE
R
PE
R
PE
R
PE
Notes: The main problem with the mesh topology is its long diameter that has negative effect on communication latency.
Torus topology was proposed to reduce the latency of mesh and keep its simplicity.
The only difference between torus and mesh topologies is that the switches on the edges are connected to the switches on the opposite edges through wrap-around channels.

## Slide 61: Direct Topology: Octagon
PE
PE
PE
PE
PE
PE
PE
PE
SW
Notes: The main problem with the mesh topology is its long diameter that has negative effect on communication latency.
Torus topology was proposed to reduce the latency of mesh and keep its simplicity.
The only difference between torus and mesh topologies is that the switches on the edges are connected to the switches on the opposite edges through wrap-around channels.

## Slide 62: Indirect Topology: Fat Tree
SW
SW
SW
SW
SW
SW
SW
PE
PE
PE
PE
PE
PE
PE
PE
Notes: The main problem with the mesh topology is its long diameter that has negative effect on communication latency.
Torus topology was proposed to reduce the latency of mesh and keep its simplicity.
The only difference between torus and mesh topologies is that the switches on the edges are connected to the switches on the opposite edges through wrap-around channels.

## Slide 63: Indirect Topology: k-ary n-fly butterfly network
SW
PE
PE
PE
PE
PE
PE
PE
PE
SW
SW
SW
SW
SW
SW
SW
PE
PE
PE
PE
PE
PE
PE
PE
SW
SW
SW
SW
Notes: The main problem with the mesh topology is its long diameter that has negative effect on communication latency.
Torus topology was proposed to reduce the latency of mesh and keep its simplicity.
The only difference between torus and mesh topologies is that the switches on the edges are connected to the switches on the opposite edges through wrap-around channels.

## Slide 64: Indirect Topology: (m, n, r) symmetric Clos network
SW
0
2
SW
0
2
SW
1
1
SW
3
5
SW
3
5
SW
4
4
SW
6
8
SW
6
8
7
7
SW
9
11
SW
9
11
SW
10
10
Notes: The main problem with the mesh topology is its long diameter that has negative effect on communication latency.
Torus topology was proposed to reduce the latency of mesh and keep its simplicity.
The only difference between torus and mesh topologies is that the switches on the edges are connected to the switches on the opposite edges through wrap-around channels.

## Slide 65: How to Select a Topology ?
Application decides the topology type
  if PEs = few tens  Mesh is recommended
  if PEs = 100 or more  Hierarchical star is recommended
Some topologies are better for certain designs than others

## Slide 66
Part II: NoC Building Blocks
Topology
Routing Algorithms
Routing Mechanisms
Control Flow
Network Interface
Router Architecture

## Slide 67: NoC Routing
Routing algorithm determine path(s) from source to destination. Routing must prevent deadlock, livelock , and starvation.

## Slide 68: Routing Deadlock
Without routing restrictions, a resource cycle can occur
  Leads to deadlock

## Slide 69: Deadlock, Livelock, and Starvation
Deadlock: A packet does not reach its destination, because it is blocked at some intermediate resource.
Livelock: A packet does not reach its destination, because it enters a cyclic path.
Starvation: A packet does not reach its destination, because some resource does not grant access (wile it grants access to other packets).

## Slide 70: Lifelock
PE
D
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
R
R
R
R
R
R
R
R
PE
PE
S
PE
R
R
R
R
R
R
R
R
Congested channel
Lifelock

## Slide 71: Deadlock
10
00
11
01
12
02
Dest 12
Dest 12
Dest 11
Dest 22
Dest 01
Dest 01
Dest 02
Dest 02
Dest 03
Dest 12
Dest 11
Dest 22
Dest 01
Dest 01
Dest 02
Dest 00

## Slide 72: Deadlock
10
00
11
01
12
02
Dest 12
Dest 12
Dest 11
Dest 22
Dest 01
Dest 01
Dest 02
Dest 02
Dest 03
Dest 12
Dest 11
Dest 22
Dest 01
Dest 01
Dest 02
Dest 00

## Slide 73: Deadlock
10
00
11
01
12
02
Dest 12
Dest 12
Dest 11
Dest 22
Dest 01
Dest 01
Dest 02
Dest 02
Dest 03
Dest 12
Dest 11
Dest 22
Dest 01
Dest 01
Dest 02
Dest 00
BLOCK
BLOCK
BLOCK
BLOCK
DEADLOCK

## Slide 74: Routing Algorithm Attributes
Number of destinations
  Unicast, Multicast, Broadcast?
Adaptivity
  Deterministic, Oblivious or Adaptive
Implementation (Mechanisms)
  Source or node routing?
  Table or circuit?

## Slide 75: Static Vs. Adaptive Routing
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
R
R
R
R
R
R
R
R
PE
PE
PE
PE
R
R
R
R
R
R
R
R
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
R
R
R
R
R
R
R
R
PE
PE
PE
PE
R
R
R
R
R
R
R
R
Static
Adaptive
Congested channel

## Slide 76: Minimal Vs. Non-Minimal
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
R
R
R
R
R
R
R
R
PE
PE
PE
PE
R
R
R
R
R
R
R
R
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
R
R
R
R
R
R
R
R
PE
PE
PE
PE
R
R
R
R
R
R
R
R
Minimal
Non-Minimal

## Slide 77: Source Vs. Distributed
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
R
R
R
R
R
R
R
R
PE
PE
PE
PE
R
R
R
R
R
R
R
R
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
R
R
R
R
R
R
R
R
PE
PE
PE
PE
R
R
R
R
R
R
R
R
Source
Distributed
E
N
E
S
E
N
N
N
L

## Slide 78: Source Vs. Distributed
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
R
R
R
R
R
R
R
R
PE
PE
PE
PE
R
R
R
R
R
R
R
R
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
R
R
R
R
R
R
R
R
PE
PE
PE
PE
R
R
R
R
R
R
R
R
E
N
E
S
E
N
N
N
L
Routing
Computation
Source
Distributed

## Slide 79: Source Vs. Distributed
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
R
R
R
R
R
R
R
R
PE
PE
PE
PE
R
R
R
R
R
R
R
R
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
R
R
R
R
R
R
R
R
PE
PE
PE
PE
R
R
R
R
R
R
R
R
N
E
S
E
N
N
N
L
Routing
Computation
Source
Distributed

## Slide 80: Source Vs. Distributed
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
R
R
R
R
R
R
R
R
PE
PE
PE
PE
R
R
R
R
R
R
R
R
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
R
R
R
R
R
R
R
R
PE
PE
PE
PE
R
R
R
R
R
R
R
R
E
S
E
N
N
N
L
Routing
Computation
Source
Distributed

## Slide 81: Source Vs. Distributed
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
R
R
R
R
R
R
R
R
PE
PE
PE
PE
R
R
R
R
R
R
R
R
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
R
R
R
R
R
R
R
R
PE
PE
PE
PE
R
R
R
R
R
R
R
R
S
E
N
N
N
L
Routing
Computation
Source
Distributed

## Slide 82: Source Vs. Distributed
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
R
R
R
R
R
R
R
R
PE
PE
PE
PE
R
R
R
R
R
R
R
R
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
R
R
R
R
R
R
R
R
PE
PE
PE
PE
R
R
R
R
R
R
R
R
E
N
N
N
L
Routing
Computation
Source
Distributed

## Slide 83: Source Vs. Distributed
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
R
R
R
R
R
R
R
R
PE
PE
PE
PE
R
R
R
R
R
R
R
R
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
R
R
R
R
R
R
R
R
PE
PE
PE
PE
R
R
R
R
R
R
R
R
N
N
N
L
Routing
Computation
Source
Distributed

## Slide 84: Source Vs. Distributed
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
R
R
R
R
R
R
R
R
PE
PE
PE
PE
R
R
R
R
R
R
R
R
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
R
R
R
R
R
R
R
R
PE
PE
PE
PE
R
R
R
R
R
R
R
R
N
N
L
Routing
Computation
Source
Distributed

## Slide 85: Source Vs. Distributed
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
R
R
R
R
R
R
R
R
PE
PE
PE
PE
R
R
R
R
R
R
R
R
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
R
R
R
R
R
R
R
R
PE
PE
PE
PE
R
R
R
R
R
R
R
R
N
L
Routing
Computation
Source
Distributed

## Slide 86: Source Vs. Distributed
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
R
R
R
R
R
R
R
R
PE
PE
PE
PE
R
R
R
R
R
R
R
R
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
R
R
R
R
R
R
R
R
PE
PE
PE
PE
R
R
R
R
R
R
R
R
L
Routing
Computation
Source
Distributed

## Slide 87: Routing examples
PE
D
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
R
R
R
R
R
R
R
R
PE
PE
S
PE
R
R
R
R
R
R
R
R
Dimension Ordered Routing (XY Routing)
X
Y

## Slide 88: Routing examples
Valiant routing algorithm
(VAL)
PE
PE
PE
PE
PE
D
PE
PE
PE
PE
PE
PE
R
R
R
R
R
R
R
R
PE
PE
S
PE
R
R
R
R
R
R
R
R
X
Y
Random Intermediate node

## Slide 89: Routing examples
ROMM
PE
PE
PE
PE
PE
D
PE
PE
PE
PE
PE
PE
R
R
R
R
R
R
R
R
PE
PE
S
PE
R
R
R
R
R
R
R
R
X
Y
Bounding Box
Intermediate node within bounding box

## Slide 90: Routing examples
O1TURN
PE
PE
PE
PE
PE
D
PE
PE
PE
PE
PE
PE
R
R
R
R
R
R
R
R
PE
PE
S
PE
R
R
R
R
R
R
R
R
X
Y
50% XY
50% YX

## Slide 91: Routing examples
Dynamic XY
(DyXY)
PE
PE
PE
PE
PE
D
PE
PE
PE
PE
PE
PE
R
R
R
R
R
R
R
R
PE
PE
S
PE
R
R
R
R
R
R
R
R
X
Y
Congested channel

## Slide 92: Summary of Routing Algorithms
Deterministic algorithms are simple and inexpensive but they do utilize path diversity and thus are weak on load balancing
Oblivious algorithms give often good results since they allow good load balancing and their effects are easy to analyse
Adaptive algorithms although in theory superior, are complex and power hungry

## Slide 93: Summary of Routing Algorithms
Latency paramount concern
  Minimal routing most common for NoC
  Non‐minimal can avoid congestion and deliver low latency
NoC researchers favor DOR for simplicity and deadlock freedom
Here we only cover unicast routing

## Slide 94
Part II: NoC Building Blocks
Topology
Routing Algorithms
Routing Mechanisms
Control Flow
Network Interface
Router Architecture

## Slide 95: Routing Mechanism
Two approaches:
  Fixed routing tables at the source or at each hop
  Algorithmic routing uses specialized hardware to compute the route or next hop at run-time
The term routing mechanics refers to the mechanism that is used to implement any routing algorithm.

## Slide 96: Table-based Routing
Two approaches:
  Source-table routing implements all-at-once routing by looking up the entire route at the source
  Node-table routing performs incremental routing by looking up the hop-by-hop routing relation at each node along the route
Major advantage:
  A routing table can support any routing relation on any topology.

## Slide 97: Table-based Routing
Example routing mechanism for deterministic source routing NoCs. The NI uses a LUT to store the route map.

## Slide 98: Source Routing
All routing decisions are made at the source terminal
To route a packet we need:
  the table is indexed using the packet destination
  a route or a set of routes are returned, one route is selected
  the route is prepended and embedded in the packet
Because of its speed, simplicity and scalability source routing is very often used for deterministic and oblivious routing

## Slide 99: Source Routing - Example
The example shows a routing table for a 4x2 torus network
In this example there are two alternative routes for each destination
Each node has its own routing table
00
10
20
30
31
21
11
01
Destination | Route 0 | Route 1
00 | X | X
10 | EX | WWWX
20 | EEX | WWX
30 | WX | EEEX
01 | NX | SX
11 | NEX | ENX
21 | NEEX | WWNX
31 | NWX | WNX
Source routing table for node 00 of 4x2 torus network
In this example the order of XY
should be the opposite, i.e. 21->12
4x2 torus network
Example:
-Routing from 00 to 21
-Table is indexed with 21
-Two routes:
NEEX and WWNX
-The source arbitrarily
selects NEEX
index
select

## Slide 100: Arbitrary Length Encoding of Source Routes
Advantage:
  It can be used for arbitrary-sized networks
The complexity of routing is moved from the network nodes to the terminal nodes
But routers must be able to handle arbitrary length routes

## Slide 101: Arbitrary Length-Encoding
Router has
  16-bit phits
  32-bit flits
  Route has 13 hops: NENNWNNENNWNN
Extra symbols:
  P: Phit continuation selector
  F: Flit continuation Phit
The tables entries in the terminals must be of arbitrary length

## Slide 102: Node-Table Routing
Table-based routing can also be performed by placing the routing table in the routing nodes rather than in the terminals
Node-table routing is appropriate for adaptive routing algorithms, since it can use state information at each node

## Slide 103: Node-Table Routing
A table lookup is required, when a packet arrives at a router, which takes additional time compared to source routing
Scalability is sacrificed, since different nodes need tables of varying size
Difficult to give two packets arriving from a different node a different way through the network without expanding the tables

## Slide 104: Example of Node-Table Routing
Table shows a set of routing tables
There are two choices from a source to a destination
Routing Table for Node 00
00
10
20
30
31
21
11
01
Note: Bold font ports are misroutes

## Slide 105: Example of Node-Table Routing
00
10
20
30
31
21
11
01
A packet passing through node 00
destined for node 11.
If the entry for (00->11) is N ,
go to 10 and (10-> 11) is S
=> 00 <-> 10 (livelock)
Livelock can occur

## Slide 106: Algorithmic Routing
Instead of using a table, algorithms can be used to compute the next route
In order to be fast, algorithms are usually not very complicated and implemented in hardware

## Slide 107: Example: Algorithmic Routing
Dimension-Order Routing
  sx and sy indicated the preferred directions
    sx=0, +x; sx=1, -x
    sy=0, +y; sy=1, -y
  x and y represent the number of hops in x and y direction
  The PDV is used as an input for selection of a route
Determines the type of the routing
Indicates which channels advance the packet

## Slide 108: Example: Algorithmic Routing
A minimal oblivious router - Implemented by randomly selecting one of the active bits of the PDV as the selected direction
Minimal adaptive router - Achieved by making selection based on the length of the respective output Qs.
Fully adaptive router – Implemented by picking up unproductive direction if Qs > threshold results

## Slide 109: Exercise
Compression of source routes. In the source routes, each port selector symbol [N,S,W,E, and X] was encoded with three bits. Suggest an alternative encoding to reduce the average length (in bits) required to represent a source route. Justify your encoding in terms of typical routes that might occur on a torus. Also compare the original three bits per symbol with your encoding on the following routes:
NNNNNEEX
WNEENWWWWWNX

## Slide 110
Part II: NoC Building Blocks
Topology
Routing Algorithms
Routing Mechanisms
Switching
Control Flow
Network Interface
Router Architecture
Part III: OASIS NoC Real Design
Next lecture