## Slide 1
Network-on-Chip
(2/2)
Ben Abdallah Abderazek
The University of Aizu
E-mail: benab@u-aizu.ac.jp
Hong Kong University of Science and Technology, March 2013

## Slide 2
Part II: NoC Building Blocks
Topology
Routing Algorithms
Routing Mechanisms
Switching
Flow Control
Router Architecture
Network Interface

## Slide 3
Part II: NoC Building Blocks
Topology
Routing Algorithms
Routing Mechanisms
Switching
Flow Control
Router Architecture
Network Interface

## Slide 4: NoC Switching
Switching techniques define the way and time of connections between input and output ports inside a switch.
Circuit switched networks reserve a physical path before transmitting the data packets
Packet switched networks transmit the packets without reserving the entire path.

## Slide 5: Circuit Switching
All resources (from source to destination) are allocated to the message prior to transport
  Probe sent into network to reserve resources
Once probe sets up circuit
  Message does not need to perform any routing or allocation at each network hop
  Good for transferring large amounts of data
    Can amortize circuit setup cost by sending data with very low per-hop overheads
No other message can use those resources until transfer is complete
  Throughput can suffer due setup and hold time for circuits

## Slide 6: Circuit Switching
Hardware path setup by a routing header or probe
End-to-end acknowledgment initiates transfer at full hardware bandwidth
tr
ts
tsetup
tdata
Time Busy
Data
Acknowledgment
Header Probe
Link
ts

## Slide 7: Circuit Switching Example
Significant latency overhead prior to data transfer
Other requests forced to wait for resources
Acknowledgement
Configuration Probe
Data
Circuit
0
5

## Slide 8: Circuit Switching Delay
  T = 3 H tr + L/b
H : time required to set up the channel and delivers the head flit
tr: serialization latency
L: time of flight
b: contention time
Note: 3 x header latency because the path from source to destination must be traversed 3 times to deliver the packet: Once in each direction to set up the circuit and then again to deliver the first flit

## Slide 9: Store & Forward Switching
Source node
Intermediate nodes
Destination node
Each node along a route waits until a packet is completely received (stored) and then the packet is forwarded to the next node
Two resources are needed
  Packet-sized buffer in the switch
  Exclusive use of the outgoing channel

## Slide 10: Store & Forward Switching
S&F switching forwards a packet only when there is enough space available in the receiving buffer to hold the entire packet.
Thus, there is no need for dividing a packet into flits. This reduces the overhead, as it does not require circuits such as a flit builder, a flit decoder, a flit stripper and a flit sequencer.
Nevertheless, such a switching technique requires a large amount of buffer space at each node. Thus, it may not be a feasible solution for embedded applications

## Slide 11: Store & Forward Switching Example
High per-hop latency
Larger buffering required

## Slide 12: Store & Forward Switching
Advantage
  While waiting to acquire resources, no channels are being held idle
Disadvantage
  Requires a large amount of buffer space at each node
  Very high latency

## Slide 13: Store & Forward Switching
Finer grained sharing of the link bandwidth
Routing, arbitration, switching overheads experienced for each packet
Increased storage requirements at the nodes
Packetization and in-order delivery requirements
Alternative buffering schemes
  Use of local processor memory
  Central (to the switch) queues

## Slide 14: Virtual Cut-through Switching
Transmission on the next channel starts directly when the new header flit is received
Channel is released after tail flit

## Slide 15: Virtual Cut-through Switching
Transmission on the next channel starts directly when the new header flit is received
Channel is released after tail flit

## Slide 16: Virtual Cut-through Switching
Transmission on the next channel starts directly when the new header flit is received
Channel is released after tail flit

## Slide 17: Virtual Cut-through Switching
Transmission on the next channel starts directly when the new header flit is received
Channel is released after tail flit

## Slide 18: Virtual Cut-through Switching
Packet-based: similar to Store and Forward
Links and Buffers allocated to entire packets
Flits can proceed to next hop before tail flit has been received by current router
  But only if next router has enough buffer space for entire packet
Reduces the latency significantly compared to SAF
But still requires large buffers
  Unsuitable for on-chip

## Slide 19: Virtual Cut-through Switching
tblocking
tw
tr
ts
Packet Header
Message Packet
cuts through
the Router
Link
Time Busy

## Slide 20: Virtual Cut-through Switching Example
Lower per-hop latency
Larger buffering required
0
5

## Slide 21: Wormhole Switching
Source node
Intermediate nodes
Destination node
Large packets are divided into small flits
An entire packet need not be buffered to move on to the next node, increasing throughput.
More efficient use of buffers than virtual cut-through
Bandwidth and Channel allocation are decoupled

## Slide 22: Wormhole Switching
Source node
Intermediate nodes
Destination node
Large packets are divided into small flits
An entire packet need not be buffered to move on to the next node, increasing throughput.
More efficient use of buffers than virtual cut-through
Bandwidth and Channel allocation are decoupled

## Slide 23: Wormhole Switching
Source node
Intermediate nodes
Destination node
Large packets are divided into small flits
An entire packet need not be buffered to move on to the next node, increasing throughput.
More efficient use of buffers than virtual cut-through
Bandwidth and Channel allocation are decoupled

## Slide 24: Wormhole Switching
Source node
Intermediate nodes
Destination node
Large packets are divided into small flits
An entire packet need not be buffered to move on to the next node, increasing throughput.
More efficient use of buffers than virtual cut-through
Bandwidth and Channel allocation are decoupled

## Slide 25: Wormhole Switching
Message are pipelined, but buffer space is on the order of a few flits
Small buffers + message pipelining  small compact switches/routers
Messages cannot be interleaved over a channel: routing information is only associated with the header
Link
Time Busy
tr
ts
twormhole
Single Flit
Header Flit

## Slide 26: Wormhole Example
6 flit buffers/input port
Blocked by other packets
Channel idle but red packet blocked behind blue
Buffer full: blue cannot proceed
Red holds this channel: channel remains idle until read proceeds

## Slide 27: Virtual Channel
Virtual channels used to combat HOL block in wormhole
Virtual channels: multiple flit queues per input port
  Share same physical link (channel)
Link utilization improved
  Flits on different VC can pass blocked packet

## Slide 28: Virtual Channel Example
6 flit buffers/input port
3 flit buffers/VC
Blocked by other packets
Buffer full: blue cannot proceed

## Slide 29: Virtual Channel Example
A: active
W: waiting
I: idle
hold information about which output virtual channel we are attempting to acquire
hold information about which input VC it is reserved by

## Slide 30: A Virtual Channel Router

## Slide 31: A Virtual Channel Router
Arriving flits are placed into the buffers of corresponding VC
Every VC of every input port has buffers to hold arriving flits

## Slide 32: A Virtual Channel Router
Arriving flits are placed into the buffers of corresponding VC
Every VC of every input port has buffers to hold arriving flits
Routing logic assigns set of outgoing VC on which flit can go
Arbitrates between competing input VC & allocates output VC

## Slide 33: A Virtual Channel Router
Arriving flits are placed into the buffers of corresponding VC
Every VC of every input port has buffers to hold arriving flits
Routing logic assigns set of outgoing VC on which flit can go
Arbitrates between competing input VC & allocates output VC
Matches successful input ports (allocated VC) to output ports
Flits at input VCs getting grants are passed to output VCs

## Slide 34: VC Arbitration: Fair Bandwidth
The virtual channels interleave their flits
This results in a high average latency

## Slide 35: VC Arbitration: Winner-Take-All
A winner-take all arbitration reduces the average latency with no throughput penalty

## Slide 36: Virtual Channels
Dest 03
Dest 22
Dest 01
Dest 00
01
11
12
02
Dest 12
Dest 11
Dest 01
Dest 02

## Slide 37: Virtual Channels
12
02
Dest 12
Dest 11
Dest 01
Dest 02
01
11
Dest 03
Dest 22
Dest 01
Dest 00

## Slide 38: Virtual Channels
12
02
Dest 12
Dest 11
Dest 01
Dest 02
01
11
Dest 03
Dest 01
Dest 00
Dest 22

## Slide 39: Virtual Channels
01
12
02
Dest 11
11
Dest 01
Dest 12
Dest 01
Dest 02

## Slide 40: Virtual Channels
01
12
02
11
Dest 01
Dest 12
Dest 01
Dest 02
Dest 11

## Slide 41: Virtual Channels
01
12
02
11
Dest 01
Dest 11

## Slide 42: Summary of Switching Techniques
Switching Technique | Communication Entity | Path Reservation | Buffer Size | Resource Utilization
Circuit Switching | Flit | Yes | Small | Poor
SAF Switching | Packer | No | Large | Good
VCT Switching | Packet | No | Large | Good
Wormhole Switching | Flit | Yes | Small | Moderate
Summary of switching techniques

## Slide 43: Break + Qs

## Slide 44
Part II: NoC Building Blocks
Topology
Routing Algorithms
Routing Mechanisms
Switching
Flow Control
Router Architecture
Network Interface

## Slide 45: Flow Control (FC)
Goal is to use resources as efficient as possible to allow a high throughput
A resource collision occurs when a packet P is unable to proceed because some resource it needs is held by another packet.
FC determines (1) how resources (Buffers and channel bandwidth) are allocated and (2) how packet collisions over resources are resolved.

## Slide 46: Node Resources
Control State
  Tracks the resources allocated to the packet in the node and the state of the packet
Buffer
  Packet is stored in a buffer before it is send to next node
Bandwidth
  To travel to the next node bandwidth has to be allocated for the packet

## Slide 47: Flow Control
NoC Flow Control can be divided into:
Bufferless flow control
  Packets are either dropped or misrouted
Buffered flow control (covered here)
  Packets that cannot be routed via the desired channel are stored in buffers
    Stop-Go,
    ACK/NACK,
    Credit-Based

## Slide 48: Bufferless flow Control
Flits can’t wait in routers.
Contention is handled by:
  Dropping and retransmitting from the source.
  Deflecting to a free output.
contention
48

## Slide 49: Bufferless Flow Control
No buffers mean less implementation cost
If more than one packet shall be routed to the same output, one has to be
  Misrouted or
  Dropped
Example: 2 packets A and B (consisting of several flits) arrive at a network node

## Slide 50: Bufferless Flow Control
Packet B is dropped and must be resended
But, there must be a protocol that informs the sending node that the packet has been dropped
  Example: Resend after no ACK has been received within a given time

## Slide 51: Bufferless Flow Control
Packet B is misrouted
No further action is required here, but at the receiving node packets have to be sorted into original order

## Slide 52: Stop-Go Flow Control
receiver
sender
Sender sends packets whenever GO signal is idle
X
Queue is
not serviced
pipelined transfer
© T.M. Pinkston, J. Duato, with major contributions by J. Filch
GO
STOP
GO
STOP
Receiver sends Issues a STOP signal when STOP threshold is reached
Sender suspends injecting flits
X
GO threshold
STOP threshold

## Slide 53: Stop-Go Flow Control
receiver
sender
Sender suspends sending packets whenever STOP signal is idle
pipelined transfer
© T.M. Pinkston, J. Duato, with major contributions by J. Filch
GO
STOP
GO threshold
STOP threshold
GO
STOP
Receiver sends Issues a GO signal when GO threshold is reached
X
Queue is
not serviced
X
Sender resumes injecting flits

## Slide 54: Ack/Nack Flow Control
Upstream node sends packets without knowing, if there are free buffers in the downstream node.

## Slide 55: Ack/Nack Flow Control
If there is no buffer available:
  the downstream node sends Nack and drops the flit
  the flit must be resent
  flits must be reordered at the downstream node
If there is a buffer available:
  the downstream node sends Ack and stores the flit in a buffer

## Slide 56: ACK/NACK
ACK/NACK propagation
Memory deallocation
NACK
Retransmission
Go-back-N
Transmission
ACK and buffering

## Slide 57: Credit-Based Flow Control
Upstream router stores credit counts for each downstream VC
Upstream router
  When flit forwarded
    Decrement credit count
  Count == 0, buffer full, stop sending
Downstream router
  When flit forwarded and buffer freed
    Send credit to upstream router
    Upstream increments credit count

## Slide 58: Credit Timeline
Round-trip credit delay:
  Time between when buffer empties and when next flit can be processed from that buffer entry
  If only single entry buffer, would result in significant throughput degradation
  Important to size buffers to tolerate credit turn-around
Node 1
Node 2
Flit departs
router
t1
Credit
Process
t2
t3
Credit
Flit
Process
t4
t5
Credit round trip delay

## Slide 59: Credit-Based Flow Control in action
receiver
sender
Sender sends packets whenever credit counter
is not zero
10
Credit counter
9
8
7
6
5
4
3
2
1
0
X
Queue is
not serviced
pipelined transfer
© T.M. Pinkston, J. Duato, with major contributions by J. Filch

## Slide 60: Credit-Based Flow Control in action
receiver
sender
10
Credit counter
9
8
7
6
5
4
3
2
1
0
+5
5
4
3
2
X
Queue is
not serviced
Receiver sends credits after they become available
Sender resumes
injection
pipelined transfer

## Slide 61: On-Off (stall-go) Flow Control
Credit: requires upstream signaling for every flit
On-off: decreases upstream signaling
Off signal
  Sent when number of free buffers falls below threshold Foff
On signal
  Send when number of free buffers rises above threshold Fon

## Slide 62: On-Off Timeline
Process
Less signaling but more buffering
  On-chip buffers more expensive than wires
Node 1
Node 2
t1
Flit
Flit
Flit
Flit
t2
Foffthreshold reached
Off
Flit
Flit
Flit
Flit
Flit
On
Process
Flit
Flit
Flit
Flit
Flit
Flit
t3
t4
t5
t6
t7
t8
Foffset to prevent flits arriving before t4 from overflowing
Fonthreshold reached
Fonset so that Node 2 does not run out of flits between t5 and t8

## Slide 63: Summary of FC
On-chip networks require techniques with lower buffering requirements
  Wormhole or Virtual Channel flow control
Dropping packets unacceptable in on-chip environment
Complexity of flow control impacts router microarchitecture

## Slide 64: Summary of FC
Ack/Nack: is rarely used because of its buffer and bandwidth inefficiency.
Credit-based: Used in systems with small numbers of buffers.
On/Off : Used in systems that have large numbers of flit buffers.

## Slide 65
Part II: NoC Building Blocks
Topology
Routing
Switching
Virtual Channels
Flow Control
Router Architecture
Network Interface

## Slide 66: Typical Virtual Channel Router
A router functional blocks can be divided into:
Data path: handles storage and movement of a packets payload
    Input buffers , Switch, Output buffers
Control path: coordinating the movements of the packets through the resources of the datapath
    Route Computation, VC Allocator, Switch Allocator

## Slide 67: Typical Virtual Channel Router
The input unit contains a set of flit buffers
Maintains the state for each virtual channel
  G = Global State
  R = Route
  O = Output VC
  P = Pointers
  C = Credits

## Slide 68: Virtual Channel State Fields (Input)

## Slide 69: Virtual Channel State Fields (Output)

## Slide 70: Packet Rate and Flit Rate
The control of the router operates at two distinct frequencies
  Packet Rate (performed once per packet)
    Route computation
    Virtual-channel allocation
  Flit Rate (performed once per flit)
    Switch allocation
    Pointer and credit count update

## Slide 71: The Router Pipeline
No pipeline stalls

## Slide 72: The Router Pipeline
A typical router pipeline includes the following stages:
  RC (Routing Computation)
  VC (Virtual Channel Allocation)
  SA (Switch Allocation)
  ST (Switch Traversal

## Slide 73: The Router Pipeline
Cycle 0
  Head flit arrives and the packet is directed to an virtual channel of the input port (G = I)
no pipeline stalls

## Slide 74: The Router Pipeline
Cycle 1
  Routing computation
  Virtual channel state changes to routing (G = R)
  Head flit enters RC-stage
  First body flit arrives at router
no pipeline stalls

## Slide 75: The Router Pipeline
Cycle 2: Virtual Channel Allocation
  Route field (R) of virtual channel is updated
  Virtual channel state is set to “waiting for output virtual channel” (G = V)
  Head flit enters VA state
  First body flit enters RC stage
  Second body flit arrives at router
no pipeline stalls

## Slide 76: The Router Pipeline
Cycle 2: Virtual Channel Allocation
  The result of the routing computation is input to the virtual channel allocator
  If successful, the allocator assigns a single output virtual channel
  The state of the virtual channel is set to active (G = A
no pipeline stalls

## Slide 77: The Router Pipeline
Cycle 3: Switch Allocation
  All further processing is done on a flit base
  Head flit enters SA stage
  Any active VA (G = A) that contains buffered flits (indicated by P) and has downstream buffers available (C > 0) bids for a single-flit time slot through the switch from its input VC to the output VC
no pipeline stalls

## Slide 78: The Router Pipeline
Cycle 3: Switch Allocation
  If successful, pointer field is updated
  Credit field is decremented
no pipeline stalls

## Slide 79: The Router Pipeline
Cycle 4: Switch Traversal
  Head flit traverses the switch
Cycle 5:
  Head flit starts traversing the channel to the next router
no pipeline stalls

## Slide 80: The Router Pipeline
Cycle 7:
  Tail traverses the switch
  Output VC set to idle
  Input VC set to idle (G = I), if buffer is empty
  Input VC set to routing (G = R), if another head flit is in the buffer
no pipeline stalls

## Slide 81: The Router Pipeline
Only the head flits enter the RC and VC stages
The body and tail flits are stored in the flit buffers until they can enter the SA stage
no pipeline stalls

## Slide 82: Pipeline Stalls
Pipeline stalls can be divided into:
Packet stalls
  can occur if the virtual channel cannot advance to its R, V, or A state
Flit stalls
  If a virtual channel is in active state and the flit cannot successfully complete switch allocation due to
      Lack of flit, Lack of credit, Losing arbitration for the switch time slot

## Slide 83: Example for Packet Stall
1. Virtual-channel allocation stall
  Head flit of A can first enter the VA stage when the tail flit of packet B completes switch allocation and releases the virtual channel

## Slide 84: Example for Flit Stalls
Second body flit fails to allocate the
requested connection in cycle 5
2. Switch allocation stall

## Slide 85: Example for Flit Stalls
3. Buffer empty stall
Body flit 2 is delayed three cycles. However, since it does not have to enter the RC and VA stage the output is only delayed one cycle!

## Slide 86
Part II: NoC Building Blocks
Topology
Routing
Switching
Virtual Channels
Flow Control
Router Architecture
Network Interface

## Slide 87
Network Interface
Router
Router
Core
NI
Memory
NI
Transmitter side
Notes: 87
87

## Slide 88
Core
NI
Flit type
Destination
Source
Packet #
Packet size
stw r9, 0(r10)
Router
NI
FT
D
S
P#
PS
stw r9, 0(r10)
Flitization
Network Interface
Notes: 88
88

## Slide 89
Core
Router
NI
FT
D
S
P#
PS
stw r9, 0(r10)
Network Interface
Notes: 89
89

## Slide 90
Router
Router
Core
NI
Receiver side
Flit
Memory
NI
Network Interface
Notes: 90
90

## Slide 91
Router
NI
Memory
FT
D
S
P#
PS
stw r9, 0(r10)
stw r9, 0(r10)
Delitization
Network Interface
Notes: 91
91

## Slide 92
Router
NI
Memory
stw r9, 0(r10)
Network Interface
Notes: 92
92

## Slide 93
93
Dest
Payload
Flit
Type
Source
Dest
Payload
Flit
Type
Source
End
Body
Header
End
Body
Header
Network Interface
OASIS NoC NI
Notes: 93
93

## Slide 94: Summary
NoC is a scalable platform for billion-transistor chips.
Several driving forces behind it.
Telecommunication devices, embedded and GP domains are attractive applications for NoC.
Expected to change the way we structure and model VLSI systems.
Many open research questions.

## Slide 95
Akram Ben Ahmed, Shohei Miura, A. Ben Abdallah, Run-Time Monitoring Mechanism for Efficient Design of Network-on-Chip Architectures, to appear in the 6th International Workshop on Engineering Parallel and Multicore Systems (ePaMuS2013'), July 2013.
Akram Ben Ahmed, A. Ben Abdallah, Low-overhead Routing Algorithm for 3D Network-on-Chip, IEEE Proc. of the The Third International Conference on Networking and Computing (ICNC'12), pp. 23-32, 2012.
Akram Ben Ahmed, A. Ben Abdallah, LA-XYZ: Low Latency, High Throughput Look-Ahead Routing Algorithm for 3D Network-on-Chip (3D-NoC) Architecture, IEEE Proceedings of the 6th International Symposium on Embedded Multicore SoCs (MCSoC-12), pp. 167-174, 2012.
Akram Ben Ahmed, A. Ben Abdallah, ONoC-SPL Customized Network-on-Chip (NoC) Architecture and Prototyping for Data-intensive Computation Applications, IEEE Proceedings of The 4th International Conference on Awareness Science and Technology, pp. 257-262, 2012.
A. Ben Ahmed, A. Ben Abdallah, Efficient Look-Ahead Routing Algorithm for 3D Network-on-Chip (3D-NoC),IEEE Proceedings of the 6th International Symposium on Embedded Multicore SoCs (MCSoC-12,) pp. 167-174,2012.
R. Okada, Architecture and Design of Core Network Interface for Distributed Routing in OASIS NoC, Technical Report, ASL- Parallel Architecture Group, School of Computer Science and Engineering, The University of Aizu, March 2012.
A. Ben Ahmed, A. Ben Abdallah, K. Kuroda,Architecture and Design of Efficient 3D Network-on-Chip (3D NoC) for Custom Multicore SoC, IEEE Proc. of the 5th International Conference on Broadband, Wireless Computing, Communication and Applications (BWCCA-2010), pp.67-73, Nov. 2010. (best paper award) (slides)
K. Mori, A. Esch, A. Ben Abdallah, K. Kuroda, Advanced Design Issues for OASIS Network-on-Chip Architecture, IEEE Proc. of the 5th International Conference on Broadband, Wireless Computing, Communication and Applications (BWCCA-2010),pp.74-79, Nov. 2010. slides
T. Uesaka, OASIS NoC Topology Optimization with Short-Path Link, Technical Report, Systems Architecture Group,March 2011
K. Mori, A. Ben Abdallah, OASIS NoC Architecture Design in Verilog HDL, Technical Report,TR-062010-OASIS, Adaptive Systems Laboratory, the University of Aizu, June 2010. slides
Shohei Miura, Abderazek Ben Abdallah, Kenichi Kuroda, PNoC: Design and Preliminary Evaluation of a Parameterizable NoC for MCSoC Generation and Design Space Exploration, The 19th Intelligent System Symposium (FAN 2009), pp.314-317, Sep.2009.
Kenichi Mori, Abderazek Ben Abdallah, Kenichi Kuroda, Design and Evaluation of a Complexity Effective Network-on-Chip Architecture on FPGA, The 19th Intelligent System Symposium (FAN 2009), pp.318-321, Sep. 2009.
A. Ben Abdallah, T. Yoshinaga and M. Sowa, "Mathematical Model for Multiobjective Synthesis of NoC Architectures", IEEE Proc. of the 36th International Conference on Parallel Processing, Sept. 4-8, 2007.
A. Ben Abdallah, Masahiro Sowa, "Basic Network-on-Chip Interconnection for Future Gigascale MCSoCs Applications: Communication and Computation Orthogonalization", JASSST2006, Dec. 4-9th, 2006.
Book: Multicore Systems-on-Chip: Practical Hardware/Software Design, 2nd Edition, Author: A. Ben Abdallah, Publisher: Springer, (2013) , ISBN-13: 978-9491216916. [Amazon]
OASIS2 NoC Chip
References